## Slide 2
Introduction
  Barcelona Climate Plan has an action line with the purpose of avoiding excessive heat to citizens.
  Cool Walks is a tool that generates fresh and cool routes through sidewalks and pedestrian crossings while using modeled shades throughout the day.
  Cool Walks guides you through the city preventing excessive heat.
  Check it yourself at:
  http://www2.bcnregional.com/

## Slide 3
How it works…

## Slide 4
Pick the origin and destination of your walk
Pick the time of the day
Zoom in / out
Shades between 10:00 and 10:30
Shades between 13:30 and 14:00
Shades between 17:00 and 17:30
Pick the route mode
Shortest path: I don't care about sunlight, I want to get there as soon as possible!
Shady path: I want to get there fast but staying cool
Vampire mode on: Avoid direct sunlight at all costs!
If you are thirsty, bring your route through a drinking fountain on your way
If you need a shelter, bring your route through a place to take shelter during high temperatures
How it works…

## Slide 5
Information about the different parts of the routing tool and how to use it
How it works…

## Slide 6
Information about used data and downloading link
How it works…

## Slide 7
Route Statistics
  Yes, it is responsive!
How it works…

## Slide 8
Video Demo

## Slide 9
Shade modeling and network building
Steps Summary
  3D model of our area of interest using LIDAR data
  Calculation of all shades during a whole day
  Network for pedestrians using all sidewalks, crossings and open public spaces
  Public space surface
  Green shading from trees
  Shading statistics at public surface
  Network impedance: routing “cost” for each mode and time of day

## Slide 10
App architecture
  Generation of a custom Web Map Service
  Network data with cost impedance is stored in a Spatialite database
  The interactive web map was built on the leaflet.js library
  Route generation makes use of the Spatialite “Virtual Network” module

## Slide 11
Public datasets
  Street trees from Open Data BCN
    https://opendata-ajuntament.barcelona.cat/data/en/dataset/arbrat-viari
  Zone trees from Open Data BCN
    https://opendata-ajuntament.barcelona.cat/data/en/dataset/arbrat-zona
  Vegetation index NDVI from Open Data BCN
    https://opendata-ajuntament.barcelona.cat/data/en/dataset/cobertura-vegetal-ndvi
  Drinking fountains from Open Data BCN
    https://opendata-ajuntament.barcelona.cat/data/en/dataset/fonts
  Public amenities for heat shelters from Open Data BCN
    https://opendata-ajuntament.barcelona.cat/data/en/dataset/mercats-municipals
    https://opendata-ajuntament.barcelona.cat/data/en/dataset/equipament-cultura-i-lleure
    https://opendata-ajuntament.barcelona.cat/data/en/dataset/educacio-ensenyament-reglat
  Topographic cartography from Carto BCN
    https://w20.bcn.cat/cartobcn/default.aspx?lang=en
  LIDAR data from Geoportal AMB
    https://geoportalcartografia.amb.cat/AppGeoportalCartografia2/index.html
  Sentinel-2 data from ESA
    https://scihub.copernicus.eu/dhus/#/home